## Slide 1: Low Area ANN Architecture with Stochastic Computing and a Simplified Sigmoid Function
Huy-Hung Ho, Xuan-Thuan Nguyen, Van-Thuat Nguyen, Van-Dung Nguyen
Key Laboratory for Smart Integrated Systems (SISLAB),
VNU University of Engineering and Technology (VNU-UET)

## Slide 2: Context and Motivation
Big Systems
IoT Devices
Constraint
Small area
Low power
Lifecycle
Reduce area cost
Backpropagation algorithm
Hardware implementation
Large models
High complexity
Training Time
Notes: LeNet (1998) AlexNet (2012) OverFeat (2013) VGGNet (2014) GoogleNet (2014) ResNet (2015)

## Slide 3: Outline
Context and Motivation
Proposed design
Evaluation
Conclusion

## Slide 4: Proposed Design
Reference model of LSI Contest
  Fixed size 2-3-2 architecture
  Sigmoid function LUT: high area cost
  Complex operators
Weighted input
Additions
Multiplications
Sigmoid function
Proposed design
  Parameterized ANN architecture (Backpropagation)
  Optimized Sigmoid Function
    Lower LUT memory
  Forward ANN use Stochastic Computing
    Replacing Addition, Multiplication by Logic gate
Low area cost
High frequency
Notes: High-cost area

## Slide 5: Optimized Sigmoid function
 | Conventional LUT sigmoid | Proposed sigmoid
MSE |  | 
Area (cell) | 85 | 67 ( -21.18% )
 | Conventional LUT sigmoid | Proposed sigmoid
MSE |  | 
Area (cell) | 85 | 67 ( -21.18% )
Conventional Method
  PWL (piecewise nonlinear approximation)
  Lookup table (8-bit LUT)
  Separating different regions
    Only function
Proposed Sigmoid Function
  3 different regions
    Constant region
    Linear region
    Non-linear region
      5-bit LUT & 3-bit LUT
Evaluation
MSE: Mean square error

## Slide 6: Forward ANN use Stochastic Computing
Stochastic computing (SC)
  Process data in the form of digitized probabilities
Stochastic Number Generation (SNG)
SC Multiplication
SC Scale Addition
Weighted input
Additions
Multiplications
Sigmoid function
Logic gate,
MUX
Stochastic Computing domain
=(+)/2
1,0,0,1,0,0,0,0
LFSR
>
SNG
LFSR: Linear Feedback Shift Register
[Lee2017eeh]

## Slide 7: Forward ANN use Stochastic Computing (cont.)
Conventional architecture
Proposed SC architecture
 | 8-bits | 10-bits
Latency |  | 
MSE | 2.03 | 
 | 8-bits | 10-bits
Latency |  | 
MSE |  | 
Forward ANN Simulation with SC length
MSE: Mean square error

## Slide 8: Outline
Context and Motivation
Proposed design
Evaluation
Conclusion

## Slide 9: Evaluation
 | LSI Contest | Our proposed (8-bit SC length)
Frequency (MHz) | 182 | 357
Slice LUTs | 814 | 738
Slice Registers | 528 | 450
Mux | 60 | 75
DSP | 12 | 0
Area (cell) | 2059 | 1627 ( -20.98% )
Latency | 4 | 
 | LSI Contest | Our proposed (8-bit SC length)
Frequency (MHz) | 182 | 357
Slice LUTs | 814 | 738
Slice Registers | 528 | 450
Mux | 60 | 75
DSP | 12 | 0
Area (cell) | 2059 | 1627 ( -20.98% )
Latency | 4 | 
Environment
  VHDL language
  Vivado Xilinx Tool
  Xilinx FPGA VC707 28nm
2-3-2 Forward Model
  Low area cost
  High frequency
  Do not use DSP
  High latency
Verification Implementation
2-3-2 forward ANN architecture evaluation
Real Fixed-point
Proposed Design
Fixed-point Real
Math Equation
Input
(real value)
MSE
MSE: Mean square error

## Slide 10: Conclusion
Contest Requirement
  2-3-2 ANN architecture with 5 sets of inputs
Proposed Design
  Parameterized 2-3-2 ANN architecture
  Simplified Sigmoid architecture
    21.18% area cost
  Forward architecture use Stochastic computing
    20.98% area cost (compared to Contest reference model)
  Limitation: High latency
Future work
  Apply Stochastic Computing for Backward module
  Reduce more area cost

## Slide 11
Thank you for your attention

## Slide 12
Backup slide

## Slide 13: Simplified Sigmoid Function Architecture
Multiplexer divide and select the regions
2 LUT 32-bit and 2 LUT 8-bit for range and
Replacing multiplication by approximated the 2-bit shift right logic
Weighted input range | Decode Selector | Output
 | 000000 | 0.999023
 | 100000 | 0.984375
 | 110000 | LUT
 | 111000 | 
 | 111100 | LUT
 | 111110 | 0.015625
 | 111111 | 0.0
Weighted input range | Decode Selector | Output
 | 000000 | 0.999023
 | 100000 | 0.984375
 | 110000 | LUT
 | 111000 | 
 | 111100 | LUT
 | 111110 | 0.015625
 | 111111 | 0.0

## Slide 14: 2-3-2 Forward architecture use Stochastic Computing
Our proposed architecture using SC
Reference architecture
of LSI Contest