## Slide 1: Accurate and Low Complex Cell Histogram Generation By Bypass The Gradient of Pixel Computation
Huy-Hung Ho, Ngoc-Sinh Nguyen, Duy-Hieu Bui, Xuan-Tu Tran
Key Laboratory for Smart Integrated Systems (SISLAB),
VNU University of Engineering and Technology (VNU-UET)
Notes: Now, don’t let you have to wait long. I will present the our paper: …

## Slide 2: Outline
Context and motivation
Cell histogram generation
Hardware implementation
Evaluation

## Slide 3: Object detection with HOG
Object detection/recognition
  Advanced driver-assistance systems
  Unmanned aerial vehicle
  AI, robot…
Automotive: pedestrian detection
Automotive:
vehicle detection
Search:
image categorization
Histograms of Oriented Gradients (HOG)
  High accuracy: 96.6%
  High complex non-linear operation
Notes: Hệ thống hỗ trợ lái xe nâng cao (ADAS) - Điều khiển tự động trong máy bay không người lái (UAV) -Dây chuyền sản xuất tự động, tương tác người và máy tính, robot…
HOG: pioneered by DALAL and TRIGGS, the most popular methods for feature extraction, based on counting occurrences of gradient orientation in localized portions of an image

## Slide 4: HOG algorithm - 3 phases
Block normalization
Cell histogram generation
SVM classification
Cell
(8 x 8 pixels)
1
Cell gradient
Cell histogram
Block
(2 x 2 cells)
Block HOG
HOG features
SVM weights
Chart: Power consumption in FPGA implementation
| Cell histogram generation | SVM classification | Histogram normalization | Controller
Power consumption in FPGA implementation | 113.55 | 62.15 | 13.81 | 7.48
Chart: Power consumption in FPGA implementation
| Cell histogram generation | SVM classification | Histogram normalization | Controller
Power consumption in FPGA implementation | 113.55 | 62.15 | 13.81 | 7.48
[Mizuno 2013]
High cost in Cell histogram generation

## Slide 5: Outline
Context and motivation
Cell histogram generation
  Conventional cell histogram generation
  Previous works
  Our proposed method
Hardware implementation
Evaluation

## Slide 6: Conventional cell histogram generation
Cell gradient vectors
Difference pixel
Gradient
(magnitude and orientation)
Chart: 
| 10 | 30 | 50 | 70 | 90 | 110 | 130 | 150 | 170
Series 1 | 0.1 | 8.2 | 9.5 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
Cell
(8 x 8 pixels)
Voting bin
Chart: 
| 10 | 30 | 50 | 70 | 90 | 110 | 130 | 150 | 170
Series 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 7: Previous works
This phase very complex, some researches opmtimized it.
First, gradient magitude calculation: square, square root.
Look-up table
Cordict
L1-Norm
Bin’s boundary angles, determinate
is constant

## Slide 8: Previous works
Look-up table
Cordict
L1-Norm
Bin’s boundary angles,
determinate
is constant
Kadota2009, Peker2011 use Look-up table for fast calculation.
But LUT requires very high area cost.
Look-up table

## Slide 9: Previous works
Look-up table
Cordict
L1-Norm
Bin’s boundary angles,
determinate
is constant
Landola2016, Suleiman2016 use L1-norm instead of L2-norm.
This method reduce the accuracy.
L1-Norm

## Slide 10: Previous works
Look-up table
Cordict
L1-Norm
Bin’s boundary angles,
determinate
is constant
Chen2014, Hsiao2016 used SRA (Square root approximation technique).
Similary, it also reduce the accuracy level.

## Slide 11: Previous works
Look-up table
Cordict
L1-Norm
Bin’s boundary angles,
determinate
is constant
For gradient orientation, Landola2015 used full LUT
for inverse tangent and consumed 256KB memory.
Look-up table

## Slide 12: Previous works
Look-up table
Cordict
L1-Norm
Bin’s boundary angles,
determinate
is constant
Takaghi2013 used CORDIC to avoid high memory.
But CORDICT require more time.
Cordict

## Slide 13: Previous works
Look-up table
Cordict
L1-Norm
Bin’s boundary angles,
determinate
is constant
All previous papers used fixed weights for voting magnitude.
That leads to the error.
is constants

## Slide 14: Previous works
Chen2014, Hsiao2016 determined without .
But this method has the potentially wrong orientation.
Constant
Bin’s boundary angles,
determinate
Look-up table
Cordict
L1-Norm
Bin’s boundary angles,
determinate

## Slide 15: Our proposed method
Avoid non-linear operation completely.
A new method

## Slide 16: Our proposed method
Determine
Determined 2 quantized orientation fast like Chen2013.
But we determine quantized orientation exactly.
is almost like
We use
to calculate gradient magnitude of two bins exactly.
Converting all of multications and division with constant
into form of shifts and additions.
Constant

## Slide 17: Outline
Context and motivation
Cell histogram generation
Hardware implementation
Evaluation

## Slide 18: Proposed hardware implementation
Proposed cell histogram generation include 4 states.
It usages 30 shifts and 40 additions.
PIX2BIN
clk
rst
+
|dx|
sign(dx)
dx
-
+
+
|dy|
sign(dy)
dy
-
+
clk, rst
b1,b2 is magnitude * sin (20)
is angle, which are encoded to bin position

## Slide 19: Outline
Context and motivation
Cell histogram generation
Hardware implementation
Evaluation

## Slide 20: Evaluation
 |  | Memory | Timming | Accurate
Basic cell hisogram generation |  | - | - | 100%
Previous works | Lookup table – Kadota2009, Peker2011 | - - | + + | - -
 | Magnitude approximations – Chen2013, Hsiao2016, Patent2015 | + |  | --
 | L1-norm instead of L2-norm – Landola2016, Suleman2016 | + |  | -
 | CORDIC - Takagi2013 |  | - | 
 | Bin’s boundary angles – Chen2013, Hsiao2016 |  |  | < 98%
Our Proposed |  | + | + | 98%

## Slide 21: Evaluation
Complexity: 30 additions + 40 shifts
Area: 3.57 KGEs (in NanGate 45nm)
Throughput: 0.4×10^6 pixel/s
Max frequency: 400 MHz
Error: < 2%
References | Approach | Areas (KGates) | Frequency
Chen2014 | Square root approx Bin’s boundary angles | 85.5 | 167 MHz (all HOG)
Hsiao2016 | Square root approx Bin’s boundary angles | 29.1 | N/A
Munteanu2016 (patent) | Square root approx Bin’s boundary angles | 20 | Max. 400 MHz
Our proposed | Bypass gradient of pixel calculation Improved bin’s boundary angles | 3.57 | Max. 400 MHz
Error compare to absolute floating point

## Slide 22
Thank you for your attention

## Slide 23
Backup slides

## Slide 24: Determining 2 quantized orientation
Chart: 
| 10 | 30 | 50 | 70 | 90 | 110 | 130 | 150 | 170
Series 1 | 0.1 | 8.2 | 9.5 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
Symmetry about angle
Use shift and comparator

## Slide 25
Chart: 
| 10 | 30 | 50 | 70 | 90 | 110 | 130 | 150 | 170
Series 1 | 4.3 | 2.5 | 3.5 | 4.5 | 1.2 | 3.2 | 1.9 | 3.2 | 4.1

## Slide 26: Conventional cell histogram generation
Chart: 
| 10 | 30 | 50 | 70 | 90 | 110 | 130 | 150 | 170
Series 1 | 0.1 | 8.2 | 9.5 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
Cell
(8 x 8 pixels)
Cell gradient vectors
Difference pixel
Gradient (magnitude and angle)
Voting bin

## Slide 27: Previous works
Look-up table
Kadota2009, Peker2011 use Look-up table for fast calculation.
But LUT requires very high areas cost.
Chen2013, Hsiao2016 used SRA (Square root approximation technique).
However, this model reduce the accuracy level.
Landola2016, Suleiman2016 use L1-norm instead of L2-norm.
Cordict
L1-Norm
Bin’s boundary angles, determinate
Takaghi2013 used CORDIC to avoid high memory.
But CORDICT require more time.
is constant
Fixed weight for voting: reduce accuracy.
This phase very complex, some researches opmtimized it.
First, gradient magitude calculation: square, square root.
For gradient orientation, Peker2011 use combined the LUT and piece-wise approximations.

## Slide 28: Approximate Computing
Cordict
Look-up table
Bin’s boundary angles, determinate
L1-Norm
is constant