## Slide 1: Accurate and Low Complex Cell Histogram Generation By Bypass The Gradient of Pixel Computation
NAFOSTED Conference on Information and Computer Science (NICS)
Huy-Hung Ho, Ngoc-Sinh Nguyen, Duy-Hieu Bui, Xuan-Tu Tran
Key Laboratory for Smart Integrated Systems (SISLAB),
VNU University of Engineering and Technology (VNU-UET)

## Slide 2: Outline
Context and motivation
Cell histogram generation
Proposed cell histogram generation
Hardware implementation & evaluation
Conclusion

## Slide 3: Object detection with HOG
Object detection/recognition
  Advanced driver-assistance systems
  Unmanned aerial vehicle
  AI, robot…
Automotive: pedestrian detection
Automotive:
vehicle detection
Search:
image categorization
Histograms of Oriented Gradients (HOG)
  High accuracy: 96.6%
  High complex non-linear operation
HOG Features

## Slide 4: HOG algorithm - 3 phases
Block normalization
Cell histogram generation
SVM classification
Cell
(8 x 8 pixels)
1
Cell gradient
Cell histogram
Block
(2 x 2 cells)
Block HOG
HOG features
SVM weights
High cost in Cell histogram generation
[Mizuno-2013]
Chart: Power consumption in FPGA implementation
| Cell histogram generation | SVM classification | Histogram normalization | Controller
Power consumption in FPGA implementation | 113.55 | 62.15 | 13.81 | 7.48

## Slide 5: Outline
Context and motivation
Cell histogram generation
  Conventional cell histogram generation
  Approximate models
Proposed cell histogram generation
Hardware implementation & evaluation
Conclusion

## Slide 6: Outline
Context and motivation
Cell histogram generation
  Conventional cell histogram generation
  Approximate models
Proposed cell histogram generation
Hardware implementation & evaluation
Conclusion

## Slide 7: Conventional Cell Histogram Generation Process
Vertical Gradient
Horizontal Gradient
Image
Magnitude
Angle
Gradient M
Voting

## Slide 8: Gradient approximations
Magnitude calculation
  L1-norm formula: reduce the accuracy [Iandola2015, Suleiman2016]
  Square root approximation technique [Chen2014, Hsiao2016]
Angle calculation
  LUT for inverse tangent: up to 256KB memory [Iandola2015]
  Combination of piece-wise and LUT: still consume large memory [Peker2011]
  CORDIC: too much iteration [Takaghi2013]
  Angle boundary: [Chen2014, Hsiao2016 ]
    
  but, no information for the voting step.
Vertical Gradient
Horizontal Gradient
Image
Magnitude
Angle
Gradient M
Voting

## Slide 9: Outline
Context and motivation
Cell histogram generation
Proposed cell histogram generation
Hardware implementation & evaluation
Conclusion

## Slide 10: Ideas
Angle boundary for detecting two voted angles
  
Computing magnitude of and
  No calculating the real gradient magnitude M of pixel
  No voting
  Solving the pixel’s gradient in Ox and Oy direction and the equality of two voted bins
Vertical Gradient
Horizontal Gradient
Image
Magnitude
Angle
Gradient M
Voting
Angle boundary
Computing magnitude

## Slide 11: Detecting angle of two voted bins
  Angle boundary
  
The nearest smaller |  | The nearest greater
 | 10 | 
 | 30 | 
 | 50 | 
 | 70 | 
 | 90 | 
 | 10 | 
 | 30 | 
 | 50 | 
 | 70 | 
 | 90 | 

## Slide 12: Calculating magnitude of two voted bin
Solving the pixel’s gradient in Ox and Oy direction and the equality of two voted bins
  Where:
  is constant angle in set HOG features;
  is gradient on horizontal and vertical gradient

## Slide 13: Dataflow of proposed method
Computing horizontal, vertical gradient
Detecting angle range or angles of two voted bins
Calculating magnitudes of two voted bins
Converting angle into left side of Oy

## Slide 14: Outline
Context and motivation
Cell histogram generation
Proposed cell histogram generation
Hardware implementation & evaluation
Conclusion

## Slide 15: Hardware Implementation
Angle and Magnitude Calculation
Step 1
Step 2
Step 3
Step 4
clk
rst
4
/
/
17
/
17
/
8
/
8
/
8
/
8
/
Inputs: 4 pixels with 8-bit length
Output: 2 bins with 8-bit fractional part

## Slide 16: Hardware Implementation (cont)
Angle and Magnitude Calculation
Step 1
Step 2
Step 3
Step 4
clk
rst
4
/
/
17
/
17
/
8
/
8
/
8
/
8
/

## Slide 17: Angle and Magnitude Calculation
Angle and Magnitude Calculation
Step 1
Step 2
Step 3
Step 4
clk
rst
4
/
/
17
/
17
/
8
/
8
/
8
/
8
/
4
/
/
17
/
17
/

## Slide 18: Our proposed method
Determine
Determined 2 quantized orientation like Chen2013.
But we determine quantized orientation exactly.
is almost like
  Solving the equality of two voted bins and the pixel’s gradient
  in Ox and Oy direction.
Converting all of multications and division with constant
into form of shifts and additions.
Constant

## Slide 19: Evaluation Methodology
Software simulation
  C++
Hardware simulation
  VHDL
Hardware implementation
  NanGate 45nm Synopsys tool

## Slide 20: Evaluation
Complexity: 30 additions + 40 shifts
Area (nanGate 45nm): 3.57 Kgates
Throughput: 1 pixel / 1 cycle
Max frequency: 400 MHz
Reconstructing error: < 2%
References | Approach | Areas (Kgates) | Frequency
Chen2014 | Square root approx Boundary angles | 85.5 | 167 MHz (all HOG)
Hsiao2016 | Square root approx Boundary angles | 29.1 | N/A
Munteanu2016 | Square root approx Boundary angles | 20 | Max. 400 MHz
Our proposed | Boundary angles Bypass gradient magnitude | 3.57 | Max. 400 MHz
48 fps with 4K UHD resolution

## Slide 21: Conclusion
Contribution
  Proposed a new methodology to calculate two bins of a pixel
    No non-linear operation
    High accuracy
  Hardware implementation
    Reduce the area by 81.2% compare to state-of-the-art
Future work
  Applied full HOG for human detection devices

## Slide 22: References
  K. Takagi, K. Mizuno, S. Izumi, H. Kawaguchi, and M. Yoshimoto, “A sub-100-milliwatt dual-core HOG accelerator VLSI for real-time multiple object detection,” in 2013 IEEE International Conference on Acoustics, Speech and Signal Processing.
  K. Mizuno, Y. Terachi, K. Takagi, S. Izumi, H. Kawaguchi, and. Yoshimoto, “Architectural Study of HOG Feature Extraction Processor for Real-Time Object Detection,” in 2012 IEEE Workshop on Signal Processing Systems.
  R. Kadota, H. Sugano, M. Hiromoto, H. Ochi, R. Miyamoto, and Y. Nakamura, “Hardware Architecture for HOG Feature Extraction.”
  F. N. Iandola, M. W. Moskewicz, and K. Keutzer, “libHOG: Energy- Efficient Histogram of Oriented Gradient Computation,” in IEEE 18th International Conference on Intelligent Transportation Systems
  A. Suleiman and V. Sze, “An Energy-Efficient Hardware Implementation of HOG-Based Object Detection at 1080HD 60 fps with Multi-Scale Support,”
  S.-F. Hsiao, J.-M. Chan, and C.-H. Wang, “Hardware design of histograms of oriented gradients based on local binary pattern and binarization,” in 2016 IEEE Asia Pacific Conference on Circuits and Systems (APCCAS)
  P.-Y. Chen, Chien-Chuan Huang, Chih-Yuan Lien, and Yu-Hsien Tsai, “An Efficient Hardware Implementation of HOG Feature Extraction forHuman Detection,”
  Munteanu, “A Method for producing a histogram of oriented gradients,” Patent Patent No. WO2 016 083 002.
  M. Peker, H. Altun, and F. Karakaya, “Hardware emulation of HOG and AMDF based scale and rotation invariant robust shape detection,” in 2012 International Conference on Engineering and Technology (ICET)

## Slide 23
Thank you for your attention

## Slide 24: Approximate Computing
Cordict
Look-up table
Bin’s boundary angles, determinate
L1-Norm
is constant